## Slide 1
The role of raw materials, packaging materials and process parameters in driving quality improvement of Promasidor Nigeria's products

## Slide 2
Training objectives
The training is expected to enable participants understand the following:
  What raw materials are
  Key considerations in the selection of raw materials
  The raw materials used in Promasidor Nigeria’s products
  The key consideration in the selection of raw materials.
  The key QA processes in raw material handling
  The process flow chart for entrance quality control tests
  The quality performance Metrics for raw material management.
  What packaging materials are
  Functions of packaging
  Categories of packaging materials
  Selection of packaging materials
  Cowbell Evap canning line process flow and quality control system.

## Slide 3
Table of Content
Raw materials
Raw Material Selection
Considerations in Selection of Raw Materials
Raw Materials Used In Promasidor Nigeria
QA Processes in Raw Material Handling
Entrance Control Quality Requirements For Raw Materials
Process Flow Chart for Entrance Quality Control Tests
Quality Performance Metrics For Raw Material Management Management.
Promasidor Nigeria Raw Material Vendor Quality Management Processes
Introduction to packaging
Functions of packaging
Types of packaging materials
Categories of packaging materials
Selection of packaging materials
Cowbell Evap canning line process flow and quality control system

## Slide 4
Raw materials, including ingredients, processing aids, and packaging, are the foundation of finished food products. As such, they must meet not only your specifications, but also regulatory requirements.
Raw materials are the foundation of finished food products. As such, they must meet regulatory requirements (safe and legal for your intended use) and your specifications (contribute to the functionality and quality of your process and product).
Raw Materials

## Slide 5
A description of team responsibilities helps in the understanding of the diverse expertise needed to identify key raw material characteristics.
Research and Development (R&D) – Invents the finished product to meet the customer’s expectations.
Quality – Ensures that the programs and practices will result in finished product that is safe, is legal, and meets the company standards as well as specifications outlined by R&D.
Production (from receiving to shipping) – Handles the raw materials and in-process and finished product in an appropriate manner (including equipment capability) to ensure the finished product is safe, is legal, and meets R&D’s specifications.
Sales/Marketing – Works with R&D and the customer to define and negotiate an acceptable product with an affiliated price point.
Diverse expertise needed in identification of raw materials

## Slide 6
R&D selects the appropriate raw materials based on functionality.
Functionality can encompass multiple areas, such as providing identified characteristics of the finished product (binders, thickeners, antimicrobial effects, etc.), organoleptic characteristics (flavor, color, aroma, texture), product safety characteristics (to lower the pH or water activity), and preservatives (extension of shelf life, color, or flavor retention, etc.).
Raw Material Selection

## Slide 7
Is there a raw material already in use that has the same or similar characteristics?
If so: Don’t add unnecessary complexity.
Resource: List of existing approved materials and their specifications.
Is this a raw agricultural item, commodity item, or one that has a standard of identity?
If so: Develop a general specification that can be used between multiple potential suppliers.
Resources: Supplier technical information, the standard of identity, food action defect level from regulations, comparison of different suppliers’ specifications from the Internet.
Considerations in Selection of Raw Materials

## Slide 8
1. What are the limitations on the use of the raw material?
No limits or qualifications, such as the Generally Recognized as Safe (GRAS) listing in the United States.
Use has been limited to specific products.
Limitations or ban on the use, such as genetically modified materials for organic products.
Resources: Supplier technical information, regulations for the country of sale, e.g., U.S. Code of Federal Regulations (CFR), Canadian Food Inspection Agency, European Commission, etc.
2.Are there legal, maximum levels for use, both in the country of manufacture and the country of sale/use?
Resources: Same as previous.
3. Does the raw material meet existing company or customer standards (e.g., kosher, halal, organic, gluten-free)?
Resources: Company standards, customer requirements, supplier technical information, supplier-provided certificates.
Considerations in Selection of Raw Materials Contd.

## Slide 9
Trials require close collaboration between R&D and the manufacturing team.
These examples of questions to be answered and the method for initiating discussions before, during, and after the trials will help facilitate the trial process.
Plant Discussions and Trials

## Slide 10
Does the new material present a potential safety or handling concern to the employees or the facility (such as a flammable material or an irritating powder that needs venting)?
Are there additional reporting requirements?
Occupational Health and Safety Considerations

## Slide 11
Are there potential toxic levels of the raw material? If so, how is potential purposeful abuse handled?
Food Defense Considerations

## Slide 12
Find historic information about the material via search engines (e.g., “pathogen + name of the material”; “recall + name of the material”; “foodborne illness + name of the materials”)
The food safety team assesses the potential biological, chemical, and physical hazards affiliated with the raw material (HACCP/HARPC review) as well as affiliated prerequisite programs and downstream prevention/elimination/reduction steps for identified hazards.
Determine if existing product safety measures are circumnavigated (e.g., the particle size is too large for the existing sifters or metalized packaging passing through a downstream metal detector).
Are additional processing steps necessary (e.g., an invert and clean if glass containers are the new material being used)?
Do new programs or procedures need to be developed (e.g., an allergen program and/or validation that the existing change-over procedures are effective in removing a different allergen)?
Product Safety Considerations

## Slide 13
Can the plant appropriately handle the material (e.g., is sufficient storage capacity and special equipment or preparation available)?
Is the existing equipment capable of handling the material (e.g.,granulation is too large for the dispenser)?
Facility and Equipment Capabilities

## Slide 14
Are there additional costs associated with the material, such as holding for COA review and/or in-house testing, additional labor, decreased line flexibility, increased time for changeovers, increased lead time prior to use (such as thawing, hydration and mixing, etc.)?
Will additional rotation controls be necessary for short shelf-life materials and will there be additional costs affiliated with more frequent delivery?
Material and Production Costs

## Slide 15
Flexibility in sourcing and cost
Is the material a commodity-type item that can be purchased from multiple sources? If so, compare existing specifications from multiple suppliers; allow comparison bidding/purchasing.
Can the tolerances for characteristics be expanded to be able to purchase from more than one source or a wider range of possible, existing materials (such as granulation size for materials that are going to be dissolved or melted)?
Can purchasing find a similar functionality material that costs less or has fewer concerns?
Size and type of packaging based on forecast use Typically, the larger the container purchased, the cheaper the cost-per-pound. However, if the forecast is for use of 100 pounds in a year, what is the appropriate-sized container to purchase? It would not make sense to purchase in 50 pound bags (multiple handlings of the package with resulting potential of damage or contamination) or in a Super-Sak (with destruction of, or potential use of, expired materials).
Post-Trial Discussions

## Slide 16
After the team has discussed and agreed upon the key characteristics for the raw material, the next step is to document these expectations. This can be as simple using as the dated Technical Data Sheet from the supplier. A purchase order should list the supplier’s specific name and item number for the material. A recommendation is to include the revision date of the Technical Data Sheet (with associated specifications).
As a company grows, or your requirements become more complex, the supplier’s information is expanded upon within your own specifications. At a minimum, the information should include technical and food safety information, including:
  The name of the product and the supplier’s item number.
  Components or composition of the material.
  The presence of regulated or customer-recognized food allergens.
  Organoleptic information (appearance, flavor, and aroma).
  Pertinent physical, chemical, and microbiological information.
  Shipping and storage information.
  Shelf life.
  Handling directions.
Raw Material Specifications

## Slide 17
General name Material identification can be general for commodity-type products or those with a standard of identity, such as salt, granulated sugar, FD&C Yellow #5, and so forth. General names or descriptors ease use and sharing specifications, especially when soliciting and comparing prices between multiple suppliers.
Material-specific name A product-specific name or number may be assigned by the supplier when the item is a unique or proprietary material (such as with most flavors).
Item number This is the number you assign to the purchased item in order to track materials within your system.
Components The ingredient/material composition is listed in decreasing order of presence or as outlined in labeling regulations. For packaging materials, the specific composition of the packaging material would be specified, such as glass, polyethylene (PET), polypropylene (PPE), and so forth.
Product Name

## Slide 18
Food Allergens It is not unusual for a supplier’s Technical Data Sheet to state that the material does not contain an allergen. If you are controlling more than these, ensure you receive written confirmation of the presence/absence of the allergens you are managing.
Organoleptic Information Organoleptic characteristics are tested with your senses, including visual appearance, aroma, and flavor. This brief description is typically used during the receipt or pre-use at the plant to confirm that basic expectations are met or identify issues that can be readily checked by appearance (puree rather than whole fruit), aroma (off odors such as musty or chemical), or flavor (caramelization with high fructose corn syrup or rancidity with oils).
Product Name Contd.

## Slide 19
Analytical characteristics typically require testing with instruments rather than your senses. For example, an organoleptic description of a product could be “red liquid” and the analytical information would be the colorimeter reading.
Characteristics to be outlined include those affiliated with functionality, quality, and food safety. You do not necessarily need a Certificate of Analysis or in-house testing for all of the listed characteristics, rather, these characteristics are outlined as an agreement about what you are purchasing and as a basis for discussion if concerns are identified.
Product Name Contd.

## Slide 20
As described earlier, determining the key biological, chemical, and physical parameters requires R&D and plant management to review historic information about the material, regulatory requirements, and the supplier history, as well as how the material will be handled in-house.
Food safety parameters or tolerances could include biological, chemical, or physical characteristics.
  Biological – Microbiological limits for pathogens, such as Salmonella and Listeria monocytogenes.
  Chemical – Fortification levels, sulfite levels, heavy metal content, etc.
  Physical – Size and foreign material (rocks, glass, metal, bones, etc.)
Product Name Contd.

## Slide 21
Functionality or quality parameters would include characteristics that can impact the functionality of the material or adversely impact your product.
  Biological – Microbiological limits for spoilage organisms or indicators of poor sanitation, including total plate count, yeast, mold, and coliform.
  Chemical – Characteristics such as concentration levels or purity.
  Physical – Characteristics such as viscosity, color, granulation size, insect parts, crush strength, physical measurements, etc.
Outline the appropriate conditions for shipping and storing the material. Include any special storage or handling directions, such as “do not freeze” or “store in a flame-resistant cabinet.”
Following the supplier’s storage recommendations, describe the product’s shelf-life (the supplier’s safety and quality guarantee for the product).
Determine if there are special directions for handling the material, such as if employees need to wear a face mask or other personal protective equipment (PPE) or if the material needs to be shaken before use.
Product Name Contd.

## Slide 22
A certificate of analysis (COA) is the supplier’s test results on the specific lot being provided to you. Before requiring a COA, determining the key characteristics that can fluctuate, past concerns, and compliance to specifications is essential to your product or process.
You may find that many of your raw materials, such as packaging materials and refined oils, may not need a COA, however, ensure that you are following any requirements outlined in customer or audit standards (such as Global Food Safety Initiative audits).
There may be upfront or hidden costs with requiring a COA. Ask suppliers what tests they routinely conduct or for a specified analysis if you are asking for this. There also may be costs for your receipt or review, for potentially holding the material while waiting for a result, and for an action plan if the results identify that the material does not meet your specifications.
Certificate of Analysis (COA)

## Slide 24
Preparation of ONGA seasoning powder: Blending steps
Step 1: 500kg salt + 83.98kg sugar + 5.2 kg soy lecithin at 200rpm for 1 minutes Step 2: 9L water + 75.4 kg oil + 65gm paprika at 500rpm for 7 minutes
Step 3: 171.45kg salt + 233.35kg MSG + 7.8kg Ribotide + 4.78kg Mane + 19.78kg IFF + 1.56kg IFF mod + 3.9kg citric acid + 2.6kg chili pepper + 13kg soy protein + 13kg caramel + 67.6kg corn starch + 29.9kg corn flour + 22.42kg cassava starch + 44.2kg cassava flour at 700rpm for 5 min
Step 4: blending at 1500rpm for 1 minute Step 5: Ribbon mixer
Onga cube Blending Steps

## Slide 25
The standards for validation and documentation are: Prove it, scientifically (validation) and If it is not documented, it was not done (documentation). These encompass the research information, meetings, and the team’s conclusions. For web searches, document dates, the name of the person who did the search, key words used, and the findings. Meeting documentation should capture dates, participants, the scope of the discussion, conclusions, and potential action plans.
A clear understanding of the materials being purchased is vital for suppliers and customers alike. Materials that do not meet your expectations can significantly reduce productivity, increase costs due to additional testing, rework, or destruction; and can place your product, company, customers, and consumers at risk for hazardous issues.
On the other hand, understanding the material and appropriate handling practices, as well as obtaining those that meet your expectations, increases productivity, decreases potential food safety risks, and is a key building block toward making a consistent, high-quality finished product.
Validation and Documentation

## Slide 26
Monosodium glutamate (E621): This is the sodium salt of glutamic acid. Glutamate is a naturally occurring amino acid that is found in nearly all food. MSG added to food produces a flavoring function similar to the glutamate that occurs naturally in foods. It acts as a flavor enhancer and add a fifth taste called “Umami”, which is best described as a savory, broth-like or meaty taste. MSG is a crystalline solid and is non-hydroscopic. Consequently, they can be stored for long period of time at ambient temperature without their appearance or quality changing. The solubility of flavor enhancers is important when blending into food formulation of which MSG is soluble in water.
Ingredient Functionality (Onga cube)

## Slide 27
Caramel (E150): This is a coloring agent and an antioxidant being used in food blend. Caramel is a complex blend of fat globules in varying size grouping surrounded by a high concentrated sugar solution in which milk solids-nonfat are dispersed. Caramel colours are dark to black liquid or solid having a odor of burnt sugar and a pleasant, somewhat bitter taste. They are totally miscible with water and contain colloidal aggregates that account for most of their coloring properties and characteristic behavior toward acid, electrolytes and tannins. Caramel colour is also known to retard flavor changes that occur in some beverages as a result of sunlight. Caramel in ONGA cube helps enhance the color by adding redness as well as contribute to the darkening and controlling of brown tones.
Ingredient Functionality (Onga cube)

## Slide 28
Paprika: This is a colorful spice derived from ground peppers. It offers a variety of beneficial compounds, including vitamin A, capsaicin and carotenoid antioxidants. These substances add to the redness of blend.
Ingredient Functionality (Onga cube)

## Slide 29
Vegetable Fat: Fats alter a food appearance by creating a glossy or moist visual texture, the ability of fat to reflect light. Fat also aid in the browning process of many food, giving them an appealing brown colour. Serve as an emulsifying agent. Emulsifying fat into blend produces unique flavor and texture qualities. Fat has the unique ability to absorb and preserve flavours. It is the basic binding agent in ONGA blend.
Ingredient Functionality (Onga cube)

## Slide 30
Citric Acid: It possesses antimicrobial properties due to its acidulation and also acts as an antioxidant. It plays a huge role in enhancing flavours, boost acidity and preserve ingredients.
Soy Protein: plays a significant role in food system as a source of supplement and complementary protein and contribute functional properties such as solubility, water absorption, viscosity, emulsification, texture and anti-oxidation
Soy Lecithin (E322): Lecithin is a food additive that comes from soy. It is used as an emulsifier and also used as an antioxidant and flavour protector. Lecithin’s is a fat that is essential in the cell of the body. It is used to keep some other certain ingredients from separating out.
Chili Pepper: contains wide array of phyto-chemicals such as vitamin, phenolic and flavonoids that are important antioxidant which may reduce degenerative disease. It also adds to the mouth burn effect.
Ingredient Functionality (Onga cube)

## Slide 31
Ribotide (E635): is a flavour enhancer which is synergistic with glutamates in creating the taste of umami.
Salt: These contribute to taste and overall flavour. It is also used to distribute minor ingredients such as the flavour and colours. Salt is also effective as a preservative because it reduces the water activity of food. Grade II salt is used in Onga cube blend to achieve a smooth free flowing and not too fine particle size blend which influences the compressibility index.
Sugar: This provides bulk which impacts the mouth feel and texture of ONGA blend. The sugar are used as bulking agents/ carriers of other ingredients instead of being for their sweetening properties. By absorbing free water and increasing osmotic pressure, sugar reduces water activity in a food system resulting in reduced microbial and mould growth as well as extending the storage life of food.
Ingredient Functionality (Onga cube)

## Slide 32
Corn starch: A valuable ingredient from corn being used as thickener, gelling agent, bulking agent and water retention agent. It is added to enhance the quality of product.
Cassava starch: An edible non-toxic and functionally important food material. It advantage over other grains or root crop includes; high purity level, excellent thickening characteristics, a neutral (bland) taste, desirable texture characteristics and it contains a high concentration of starch (dry matter basis).
Ingredient Functionality (Onga cube)

## Slide 33
The efficiency of a product can be evaluated by a number of quality control parameter. Of major importance to bouillon cubes, which has been adopted by the ONGA cube factory to measure the feasibility of the raw material and process include; moisture content, blend temperature, fat temperature, bulk density, tapped density, compressibility index, hausner's ratio and sodium chloride. Most of these parameters are linked together and aimed towards ascertaining the flowability, mouldability and machinability of the blend.
Process Parameters Involved in Onga cube production

## Slide 34
Flowability is defined as the ability of granular solids and powders to flow. Flow is defined as the relative movement of a bulk of particles among neighbouring particles, or along a container wall surface. Flow characteristics are of immense significance in bulk material handling and processing, since the ease of conveying, blending, and packaging depends on them. Flow behavior is multidimensional in nature, and it depends on many physical characteristics. Some of the factors that affect flowability include;
  Particle size distribution
  Moisture
  Temperature and humidity
  Particle size
  Pressure
  Fat content
  Addition of flow agents
  Chemical composition of the particles
  Surface of the solid (silo)/ wall friction
Process Parameters Involved in Onga cube production

## Slide 35
The flowability of a powder is measured by the parameter, compressibility index (CI). This index measures the tendency of a powder to consolidate. The behavior of bulk solids under compressive stress is expressed by the compressibility index. It is used to obtain the pressure- density relationship and is calculated by:
CI = [(TD – BD)/TD ] × 100
Process Parameters Involved in Onga cube production

## Slide 36
Tapped Density and Bulk Density represent the tapped (or packed) and aerated bulk densities, respectively. The aerated bulk density is defined as the mass divided by the volume occupied by the powder including the interparticulate void volume. The tapped bulk density is obtained after tapping the container enclosing the aerated powder.
The compressibility index has an inverse relation with flowability, i.e. the more compressible is the material the less flowable it will be. A powder with a compressibility index lower than 20% is considered to have a good flowability.
Process Parameters Involved in Onga cube production

## Slide 37
Also, as a function of the bulk and tapped density, the Hausner ratio is obtained. This ratio is a useful measure of cohesion reflecting particle friction. This is the ratio of the poured density to the tapped density. Hauser showed that free flowing powders ( with low inter particular friction) had a ratio of less than 1.2 compared to more cohesive powders, and thus less free flowing, had higher values (>1.5). By this he demonstrated that this ratio is a predictive of powder flow as it is related to the inter-particulate friction. With a Hausner ratio higher than 1.4, the powder is considered a cohesive difficult to fluidize powder. Ratios lower than 1.25 characterizes a free-flowing powder.
Process Parameters Involved in Onga cube production

## Slide 38
Good flow behaviour usually means that a bulk solid flows easily, that is, it does not consolidate much and flows out of a silo or a hopper due to the force of gravity alone and no flow promoting devices are required. Products are poorly flowing if they experience flow obstructions or consolidate during storage or transport.
The flowability of a bulk solid depends on the adhesive forces between individual particles. Different mechanisms create adhesive forces. With fine-grained, dry bulk solids, adhesive forces due to van der Waals interactions play the essential role.
Process Parameters Involved in Onga cube production

## Slide 39
Whether a bulk solid flows well or poorly depends on the relationship of the adhesive forces to the other forces acting on the bulk solid. It can be shown that the influence of adhesive forces on flow behaviour increases with decreasing particle size. Thus, as a rule, a bulk solid flows more poorly with decreasing particle size. Fine-grained bulk solids with moderate or poor flow behaviour due to adhesive forces are called cohesive bulk solids.
Also, an increase in humidity, temperature as well as moisture content decreases the flowability of the blend. Regularization of these parameters are therefore important to achieve good flowability and quality cubes.
Process Parameters Involved in Onga cube production

## Slide 40
Moisture Content
This is the total amount of water present in food and it is measured by measuring the difference between the initial weight of the sample (wet weight, w) and the weight of the sample after its moisture has been removed (dry weight, d), divided by the initial wet of the sample. Then the percentage is calculated.
M.C = [(w – d) / w ] × 100%
The moisture content of the bouillon cubes should be <3.5. The moisture content plays a significant role in the freshness and stability for storage of the bouillon cubes. It defines the appropriate storage condition and shelf life of the cubes. A high moisture content may result in cube crumbling or stickiness of cubes and subsequent melting.
Process Parameters Involved in Onga cube production

## Slide 41
Entrance control tests
Warehousing practices auditing
Supplier quality management
Stock rotation management
Environmental monitoring of warehouse
Hygiene management
Pest management
QA Processes in Raw Material Handling

## Slide 42: Entrance Control Quality Requirements For Raw Materials
S/N | Key Result Area | Indicators
1. | Stock rotation | 100% compliance to FIFO/FEFO policy. No leakages Raw materials should not be laid on the bare floor but on a clean material- nylon No sign of pest infestation
2. | Quality Control Technical documents | Certificate of Analysis (CoA) must be provided (either from the vendor’s laboratory or a certified external laboratory analyst). Material Safety Data Sheet (MSDS) must be provided for all chemical based raw materials. Corresponding dates & batch number on stock and its accompanying CoA. No repetition of CoA for multiple deliveries. One unique CoA for each consignment. No falsification/cloning of CoAs.
3. | Packaging/Labelling | Properly sealed,no leakages. No signs of pest infestation. No stains,wetness,discoloration The manufacturer’s name and address,date of manufacture,expiry date,batch number,pack size,regulatory certification (NAFDAC,SON). No double labelling and contradicting information on the labels. No short or post-dating of shelf life.

## Slide 43: Process Flow Chart for Entrance Quality Control Tests
No
Yes
Warehouse Officer sends out request/awareness for raw material delivered for sampling
Lab officer checks supply for important details and reviews accompanying technical documents
Chemical lab:
Determine & prepare lab sample
Sampling of supplied material
Lab receives samples
Sample information is documented
Analysis
Microbial?
Determine lab sample size
Prepare lab sample (homogenize)
Pass remaining bulk to Chemical lab
1
1
Analyze lab sample
Collate and document results
Distribute results to warehouse team
Retain samples for reference
Generate and analyze data
End
Failed stock is evacuated by the vendor within 24 hours while QA passed stock is received into the warehouse

## Slide 44
S/N | Key Quality Process | Key Performance Indicators (Metrics)
1. | Entrance Control Tests | Monthly in-bound compliance score for each raw material supplier Number of identified food safety issues applicable to all consignments supplied by each supplier for each raw material.
2. | Good warehousing practices | Good warehousing practices (GWP) score
3. | Stock inventory management | Aging analysis of raw materials Inventory of expired raw materials.
Quality Performance Metrics For Raw Material Management

## Slide 45
S/N | Key Quality Process | Key Performance Indicators (Metrics)
4. | Environmental monitoring | Temperature of warehouse (ambient raw materials) Temperature of cold room (cold sensitive raw materials) Relative humdity of warehouse (ambient raw materials) Warehouse environmental microbial count
5. | Hygiene management | Percentage compliance to cleaning schedule in the warehouse and cold rooms Raw material elivery vehicle hygiene audit score % returns from trade traced to poor delivery truck hygiene/road worthiness. Protective Personal Protective Equipment (PPE) compliance score for warehouse operatives
6. | Pest management | Percentage compliance to the fumigation and deratization schedule for warehouses. Number of pest infested raw materials in the warehouses.
Quality Performance Metrics For Raw Material Management Management Contd.

## Slide 46
S/N | Key Quality Process | Key Performance Indicators (Metrics)
7. | Supplier Quality Management | Number of vendor audit completed. Number of food safety and quality audit gaps identified during a vendor’s audit Percentage inbound conformance score for each vendor. Turnaround time for vendor implementation of corrective and preventive action time for quality issue reported on raw material supplied.
Quality Performance Metrics For Raw Material Management Management Contd.

## Slide 47
PNG Raw Material Supplier Quality Management Processes
Supplier Development
Supplier risk assessment, risk reduction and risk monitoring.
Implementing a supplier evaluation and rating process.
Raw material specification communication to prospective vendor by Research and Development unit
Laboratory analysis of suitability samples
Bench trials of suitability samples
Plant trials of suitability
Shelf stability evaluation of finished product samples
Supplier audit
Monthly review of inbound quality conformance and communication of report by Quality Assurance department to Supply Chain
Grading system for suppliers- Grade 1- 100% inbound conformance in a six months period. Grade 2- 90-99% inbound conformance. Grade 2- Less than 90%.
Supplier facility audit
Reliability (OTIF and quality conformance)
Cycle time for resolution of complaints on quality.
Review of quality conformance on monthly basis
Process quality performance (impact on production process performance metrics- quality, machinability and wastages)
Communication of non conforming consignment for evacuation
Isolation of failed consignment in a designated location.
Technical engagement by QA unit with the vendor on root cause of non conformance.
Follow up audit visit to supplier’s facility.
Technical support by Quality Assurance unit in implementing corrective and preventive action.
Non conformance management and supplier corrective & preventative action process.

## Slide 48
Packaging role in driving quality improvement of Promasidor Nigeria’s Products

## Slide 49
One hundred years ago there was little use for packaging in the food industries.
Now, tremendous progress has been made in the development of diversified packaging materials and in the packaging equipment.
Over the last three decades, packaging has grown in volume and importance into one of the most significant areas of food production.

## Slide 50: Packaging performs five main functions
1- product containment
2- preservation and quality
3- presentation and convenience
4- protection during distribution and processing
5- provide storage history

## Slide 51
1-Product Containment
The first function of packaging is its capability of containment.
The primary purposes of packaging are containment and protection.
It is self-explanatory; liquids, semi liquids, and powders, as well as bulk solids, cannot be marketed without suitable containers.
Containment refers to holding goods in a form suitable for transport, whereas protection refers to safekeeping goods in a way that prevents significant quality deterioration.

## Slide 52
2-Preservation by Maintaining Quality
The second function of packaging is to control the local environmental conditions to enhance storage life and safety.
The main purpose of food packaging is to protect the product from surroundings and maintain the quality of the food throughout the product’s shelf life.
Product shelf life is controlled by three factors:
1-Product characteristics,
2- Packaging material properties,
3- Environment parameters.
Reactions causing deterioration in foods include enzymatic, chemical, physical, and microbiological changes. Additional problems include insects, pests, and rodents.

## Slide 53
Nutritional Quality
Packaging affects the nutritional quality of foods.
As antioxidative nutrients such as vitamins C and E are lost.
Carotenoid pigments can also be oxidized, leading to loss of color as well as loss of their beneficial effects in the body.
Lipid hydroperoxides can also result in the formation of aldehydes and other compounds with off-flavors.
Among all other functions of packaging, the protection of foodstuffs against light plays a key role particularly during storage, transport, and sales display.

## Slide 54
To achieve the best from packaging , it is important to know product characteristics, properties of individual package, storage, and distribution conditions.
Barrier properties include permeability of gases such as:
O₂ ,Co₂ ,N₂ , C₂H₄ (Ethylene), water vapor, aromas, and light. These are vital factors for maintaining the quality of foods.
packaging materials cannot be chosen solely on the basis of their barrier properties.
Barrier Properties

## Slide 55
Now various types of active substances can be incorporated into the packaging material to improve its functionality and give it new or extra functions.
Such Active packaging technologies and Antimicrobial Packaging and Edible Film are designed to extend the shelf life of foods, while maintaining their nutritional quality and safety.
Factors such as proccessability , mechanical properties and chemical resistance and interaction with product and Environmental factors, such as temperature, relative humidity, and light intensity must also be taken into account.

## Slide 56
3- Presentation and Convenience
Food labels are intended by law to provide the information that consumers need to be able to make the necessary decisions about those purchases of food.
It is important to display the product in an attractive manner to the potential buyer.
A cleverly designed and beautifully produced packaging can help sell a product, which is an essential ingredient of an effective marketing campaign . The packaging helps in distinguishing products on the shelf, which is a trait especially important when marketing low-fat or nutritional products.
For a package to be effective, it must present the product well and should do its own publicity.

## Slide 57
Changes in society, such as diminishing population pattern, increasing average age, smaller families, more leisure time, as well as improvements in the quality of life, standard of living, and general level of education, may also demand specific function of packaging.
Eating styles, such as ready-to-eat meals, snacks, and microwaveable ready meals, have been changed over the years, which need innovation in packaging.
Packaging should meet the future demand of meeting eating style of the society.
For children, the packaging might represent innovation or fun.

## Slide 58
4- Protection during Distribution and Processing
The fourth function is to protect the product during transit to the consumer.
Packaging is part of the distribution process necessary to deliver goods to the consumer and facilitate handling and transportation.
It also has affected international trade by making shipping of food products possible, allowing seasonal products to be more accessible out of season.
Packaging can handle better when there are challenges in food distribution chain, such as heat, humidity, or dew.

## Slide 59
It is important to be aware of the distribution challenges and designing of package to suit it.
In case of prepacked product, it should have the ability to stand the severity or type of process conditions , such as flexible packaging during canning, microwaveable foods, ovenable , and retortable foods.
Irradiated foods are usually prepacked prior to treatment by ionizing radiation.
Protective packaging is a term applied to packaging primarily designed to protect the goods, rather than for appearance or presentation.

## Slide 60
5-Provide Storage History
Time-temperature indicator (TTI) is effective for predicting microbial concentrations and other parameters of food quality during shipping and storage.
It helps in ensuring proper handling and provides a gauge of product quality for sensitive products in which temperature control is imperative to efficacy and safety..
TTI could be used in chilled foods to identify the temperature abuse during storage and distribution.

## Slide 61
TTIs are tags that can be applied to individual packages or shipping cartons to visually indicate whether a product has been exposed to time and temperature conditions that adversely affect the product quality.
According to the response mechanisms, TTIs can be divided into three groups: (i) biological, (ii) chemical, and (iii) physical systems
There are two issues to be considered:
One is the economics .
The other issue is knowledge of the food product.

## Slide 63
Packaging categories
1- primary packaging
2- secondary packaging
3- transit packaging
wrapping used to bundle the boxes or crates
for transport and distribution.
Primary packaging surrounds the product
and features labelling.
ease of manual movement of products.

## Slide 64
Selecting the right material
Material selection is based on:
technical properties (strength, flexibility, etc.)
fitness for purpose (moisture barrier, cushioning, etc.)
availability
manufacturing capability
cost
environmental impact
regulations

## Slide 65
Types of Packaging Materials
From skins, leaves, and bark, tremendous progress has been made in the development of diversified packaging materials and in the packaging equipment.
In general, packaging materials may be grouped into
1- rigid (wood, glass, metals, and hard plastics )
2-flexible structures. (Plastic film, foil, paper, and textiles )

## Slide 66
1- Plastics
Wide diversity and extremely broad spectrum of properties.
Plastics are relatively cheap, light, easily processed and shaped, and easy to seal.
Two major drawbacks are their permeability to gases and vapors, and the possibility of their interacting with the product.
Other components in plastics are residual monomer and oligomers, additives such as heat and light stabilizers, antioxidants, plasticizers, and UV absorbers, as well as processing aids such as lubricants, slip agents , and antistatic agents.

## Slide 67
For package sterilization, the material of choice is polypropylene (PP), which is used as the outer and inner plies of the laminate with poly-vinylidene chloride (PVDC) as the middle layer to provide an oxygen barrier.
Plastic Bags
Plastic Closures
Oven-Safe Containers
The three main plastics used are :
PP, PE (LD & HD) PS, and PET. PP is suitable for microwaves.
but now, PS low-density blends have been developed with heat deflection temperatures (HDTs) of 190°C, which is suitable for microwaves.

## Slide 68
Plastic–Food Interaction
Polymer materials are not absolute barriers.
Interactions occur between foods, packages, and polymer materials
In case of plastics, the major source of concern is the component migration.
Migration from plastics is mainly due to:
1- residual components and reactants from the manufacturing process
2- compounds formed during conversion into packaging materials and packages,
3- additives incorporated
4- adhesives used during conversion.
Other factors includes crystallinity of polymers, glass–rubber transition, environmental conditions, and composition of packaged food.

## Slide 70
Metals (Steel, Tin, Aluminum)
Steel, tin, and aluminum are used mainly for canned foods and beverages. The most common use of metals for packaging is in tin-coated steel and aluminum cans.
The principal advantages of metal cans are their strength providing mechanical protection, effective barrier properties, and resistance to high temperatures providing stability during processing.
it is an advantage for light-sensitive products.
disadvantage in that contents are: invisible, heavy mass, high cost, and tendency to interact with contents and environment (internal and external corrosion)

## Slide 71
The steel can provide almost perfect barrier protection and, due to its structural strength and ability to handle pressure, can be retorted (cooked under pressure) after sealing .

## Slide 72
Metal–Food Interaction:
Corrosion is the destructive attack on a metal through the chemical or electrochemical reaction with the environment. Since steel corrodes rapidly in the presence of acidic substances, the tin acts as a barrier.
Some cans are lacquered internally for high-acid products (pH < 3) or for products that change color in the presence of tin.
Foods that contain sulfur produce a
blackening of the tin.

## Slide 73: Glass
Advantages:
Glass containers used to be and still are considered a prestigious means of packaging, and serve for the most expensive wines, liqueurs, perfumes, and cosmetics.
It is highly inert, impermeable to gases and vapors, and amenable to the most diverse shaping. It is an excellent oxygen barrier and completely neutral in contact with foods
It has the advantage of transparency, but where required it can be given different desired colors.
It has complete as well as selective light protection properties.

## Slide 74
Disadvantages are :
fragility, heavy mass, and high energy requirement during
manufacturing.
The main uses of glass for packaging are in milk bottles, condiments, baby foods, instant coffee, and drinks.
Glass is not used for frozen products, or for ground or roasted coffee because of breakage costs and the difficulty of vacuum flushing.

## Slide 75
Timber, Cardboard, and Papers
Pulp products are widely used in food packaging in the form of different kinds of paper, paperboard, laminates, and corrugated board.
The main advantages of paper are its low cost, low mass, relatively high stiffness, and excellent printability;
the main disadvantage is its high sensitivity to moisture, reflected in close dependence on the relative humidity of the environment.
The basic raw material for papermaking is cellulose.

## Slide 76: Wood is commonly used in box construction, but the use of wood for individual packaging (such as cigars) has decreased since the advent of plastics. Examples of timber for packaging are cases, boxes, and casks for long-distance transport.
Cardboard
Timber
Choosing a carton for a specific job depends on the capacity of the carton to meet the requirements for that job.

## Slide 77
Environmental Issues
Recently, a new dimension of safety has arisen, the ecological dimension.
This means that packaging has not only to satisfy physical, chemical, and biological criteria using their life cycle as packaging, but once the original function has been fulfilled the packaging should decay without polluting the environment.

## Slide 78
Biodegradable material for packaging
Biodegradation is the process by which carbon-containing chemical compounds are decomposed in the presence of enzymes secreted by living organisms.
There are three requirements for the fast degradation process viz. temperature, humidity and type of microbes.
Acceptable bio-plastics are listed below
1- Cellulose
2- Starch
3- Poly-beta-hydroxyalkanoates (PHB): a polymer belonging to the polyesters class that are of interest as bio-derived and biodegradable plastics.
4- Polylactide Acid (PLA) plastics: derived from renewable resources, such as corn starch (in the United States and Canada), tapioca roots, chips or starch (mostly in Asia), or sugarcane (in the rest of the world). In 2010, PLA had the second highest consumption volume of any bio plastic of the world

## Slide 79
1.The Can body production process starts with the receipt of raw materials (body tin plate, copper wire, spray lacquer powder and can lids).
2.Loading the tin plate on the Cevolani (body making machine) slitting machine conveyor and make sure it is set properly and setting of copper wire. QC check the diameter of the receipt copper wire( specification:1.36-1.40mm).
3.Start the body making slitting machine.
4.The tin plate in cut into 5 strips and then in turn each of the strips is cut into 13 body blanks which form the can body.
5.The Cevolani (body making machine) robot transfers the body blanks to the body maker/welding machine. QC picks body blank samples and checks for blank size(specification:197.92-198.00mm/59.98-66.02mm) and squareness(specification: 0.00-0.05mm).
Canning Factory Process Flow and QC System

## Slide 80
6.Each blank is folded into cylinder shape and welded with copper wire along the weld margin.
7. QC checks the width of copper wire after flattening (specification: 1.75-1.85mm)
8.The welded cylinders move along in the body maker where the internal weld margin is sprayed coated with spray lacquer powder along the weld line by the powder recycling/application and lacquer system to prevent rust which can contaminate the milk filled into the cans. QC pick samples of welded cylinders, visually check the lacquer coverage, squareness of the can cylinders and measure the height (specification: 65.90-66.10mm) and also carryout weld test and confirm it okay.
9.From the body maker, the can cylinders move along a conveyor into the multicoil induction oven to “cure” the internal lacquer powder coating.
10.The cans move out of the oven along a chain conveyor, QC pick samples and check for lacquer powder coverage and dryness (curing).
Canning Factory Process Flow and QC System Contd.

## Slide 81
11.The cans move into combination machine (flanging and double seaming) where the can cylinders are flanged and double seamed with can lids. This is done in two operations; 1st operation involves flanging both ends of the cylinder while the 2nd operation bottom seam (double seamed) the lids supplied with the flanged cylinder to form the cans that are sent to the filling section during production.
QC picks different samples and checks all the parameters;
flanged cylinder height (specification:63.3-63.60mm),
flange width (specification:2.20-2.50mm),
can height bottom (specification:62.80-63.40mm),
over seam diameter (specification:63.90-64.50mm),
countersink depth bottom (specification:2.90-3.30mm),
Canning Factory Process Flow and QC System Contd.

## Slide 82
visually inspection of double seam defects such as seaming of double lids(bad seamed) knock down flange/curl (bad seamed), can body abuse/dent, distorted double seamed(bad seamed), cut over/sharp seam on each station, can blow out/cut at the welding end etc.
leak test (bottom/weld seam inspection on each station),
can body enamel rate analysis (specification:10mA maximum on 8 average cans),
seam thickness analysis (specification:0.95-1.05mm) and
carry out double seam evaluation/analysis on each station/head with the aid of seam viewer ,
  double seam evaluation parameters include:
  seam thickness( specification:0.95-1.05mm),
  seam length (specification:2.20-2.70mm),
  body hook (specification 1.70-2.10mm), end
  hook (specification :1.70-2.10mm),
  overlap( specification1.00mm minimum),
  body hook butting (specification70% minimum).
Canning Factory Process Flow and QC System Contd.

## Slide 83
However, series of different analysis is also carried out in filling section double seaming machine by QC after top seaming such as:
  seam thickness (specification0.95-1.05mm),
  can height top/bottom( specification 62.60-63.20mm),
  visual inspection of double seam circumference on each station, countersink depth (specification:2.90-3.30mm) and
Double seam evaluation on each station. Double seam evaluation parameters of top seam include
seam thickness (specification: 0.95-1.05mm),
seam length (specification: 2.20-2.70mm),
body hook (specification 1.70-2.10mm),
end hook (specification: 1.70-2.10mm), overlap (specification1.00mm minimum),
body hook butting (specification70% minimum) and visual inspection of double seam defects such as seaming of double lids(bad seamed) knock down flange/curl (bad seamed), can body abuse/dent, distorted double seamed(bad seamed), cut over/sharp seam on each station etc.
Canning Factory Process Flow and QC System Contd.

## Slide 84
If the cans parameters are not within specified ranges, engineers’ attention is called, bad cans are rejected and sent to waste.
When there is no need to send cans to filling section, cans produced are sent to the GPM Project machine (palletizing and de-palletizing, which palletize the cans for storage or de-palletize the cans and send to filling section through a conveyor.
Canning Factory Process Flow and QC System Contd.

## Slide 85
Thank you